## Slide 1
GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi1 Jisung Park1 Harun Mustafa1 Jeremie Kim1 Ataberk Olgun1 Arvid Gollwitzer1 Damla Senol Cali2 Can Firtina1 Haiyu Mao1 Nour Almadhoun Alserr1 Rachata Ausavarungnirun3 Nandita Vijaykumar4 Mohammed Alser1 Onur Mutlu1
1ETH Zürich 2Bionano Genomics 3KMUTNB 4University of Toronto
Reporter：Zhenhua Zhao Date：2023.3.14
ASPLOS’22 CCF-A

## Slide 2: Outline
Background
Motivation Studies
GenStore Design
  Overview
  GenStore-EM for Exactly-Matching Reads
  GenStore-NM for Non-Matching Reads
  GenStore Flash Translation Layer (FTL)
Evaluation
Related Work

## Slide 3: Background
  Central Dogma of Biology
  Usage of Genome Sequence Analysis
Personalized medicine
Outbreak tracing
Evolutionary studies
翻译
双螺旋
结构
碱基(AGCT)
DNA
RNA
蛋白质
生命
活动
转录
调控

## Slide 4: Background
  Read mapping：first key step in genome sequence analysis
    Aligns reads to potential matching locations in the reference genome
    For each matching location, the alignment step finds the degree of similarity (alignment score)
    Require large amounts of computationally-expensive approximate string matching (ASM) computation between reads and the reference genome due to:
      - Sequencing errors and Genetic variation
generate millions randomly sampled, inexact sub-strings of the original genome, called reads
Short read
  accuracy：99-99.9%
102 DNA base pairs
Long read
accuracy：85-90%
103 ~106 DNA base pairs
Human full DNA
3.2×109 DNA base pairs
②basecalling
①collection, preparation, and sequencing of a DNA sample in the laboratory
③Read mapping

## Slide 5: Background
  Read mapping Process
  GenStore: Filter reads that do not require alignment inside the storage system
For reference gene sequence: Build k-mer Index
For short reads:
Seeding: Determine potential matching locations (seeds) in the reference genome
Seed Filtering(Chaining): Prune some seeds in the reference genome
Alignment: Determine the exact differences between the read and the reference genome

## Slide 6: Background
  Prior works on optimizing Genome Sequence Analysis
  heuristics ASM
hardware accelerators
prior works
filters(prune reads that do not require expensive computation)
Ignore the I/O cost that most systems must pay to read the large amount of data from the storage system to main memory and computation units.

## Slide 7: Motivation Studies
Read mapping systems | Optimization technique | Evaluation Platform
Minimap2 | Baseline | AMD EPYC 7742 CPU with 1TB DDR4 DRAM
SW-filter | Filter out exactly-matching reads using SIMD | 
Ideal-ISF | In-Storage Filter (ISF) can concurrently filter out exact-matching reads inside the SSD Host CPU performs read mapping for nonfiltered reads | Simulation environment
ACC | Hardware accelerator GenCache | 
Ideal-ISF+ACC | ISF filtering out exactly matching reads inside the SSD ACC performs read mapping for non-filtered reads | 
  Perform experimental studies to understand the potential of efficient in-storage accelerators for improving the performance of genome sequence analysis applications.

## Slide 8: Motivation Studies
Configuration | Interface | Internal/External bandwidth Ratio
Low-end SSD (SSD-L) | SATA3 interface | 8 channels×1.2GB/s / 500MB/s = 19.2×
Mid-end SSD (SSD-M) | PCIe Gen3 M.2 interface | 16 channels×1.2GB/s / 3.5GB/s = 5.48×
High-end SSD (SSD-H) | PCIe Gen4 interface | 16 channels×1.2GB/s / 7GB/s = 2.74×
Idealized System | Data pre-loaded to DRAM | -
  To assess the impact of the storage subsystem on end-to-end application performance, we evaluate each of the five systems with four different configurations.(we do not evaluate DRAM for Ideal-ISF and Ideal-ISF+ACC since using in-storage processing is contradictory to pre-loading all the data to main memory)

## Slide 9: Motivation Studies
  Results & Analysis
Observation
Filtering outside SSD provides lower performance benefit because it
  1) does not reduce the data movement overhead
  2) must compete with read mapping for system resources
A HW accelerator reduces the computation bottleneck, which makes I/O a larger bottleneck in the system.

## Slide 10: GenStore
    The key idea
    Exploit low-cost in-storage accelerators to accurately filter out the reads that do not require the expensive ASM computation in read mapping, thereby significantly reducing unnecessary data movement from the storage system to main memory and processors.
    Two Challenges
        Read mapping workloads exhibit fundamentally different behavior, due to:
          read length and error rates
          the genetic variation of reads compared to the reference genome
        Existing filtering methods incur a large number of random accesses to large datasets
          NAND flash-based SSD with poor random-access performance and limited size of internal DRAM.
      Solution
        Two different filter accelerators
        Replace expensive random accesses with more efficient sequential accesses to storage devices
        Data placement inside the storage device that takes full advantage of the high internal SSD bandwidth to concurrently access large amounts of genomic data.

## Slide 11: GenStore
  Overview
  ① a single SSD-level accelerator (comparator )
  ② channel-level accelerators, each of which is dedicated to a channel (indexing,chaining PE)
  ③ The GenStore-FTL communicates with the host system and manages the metadata and data flow over the SSD hardware components

## Slide 12: GenStore
  GenStore-EM for Exactly-Matching Reads: accelerate read mapping by using an efficient in-storage filter for reads that have at least one exact match in the reference genome.
  Key Idea:sequentialize most data accesses via a carefully designed metadata structure and data layout. To do so, we design a new sorted, read-sized k-mer index structure.
    SRTable：each entry stores a read and its unique ID
    SKIndex：contains all unique readsized k-mers of the reference genome, along with each k-mer’s corresponding locations in the reference genome.

## Slide 13: GenStore
  Overall operational flow of GenStore-EM, which consists of two steps:
    Step 1. data fetching (in batched manner, double buffering)
    Step 2. exact-match filtering(using simple comparator logic in the SSD-level accelerator)
Steps 1 and 2 are performed in a pipelined manner. During filtering, GenStore-EM sends the unfiltered reads to the host system for full read mapping. This enables the concurrent filtering of reads in the SSD and read mapping of the unfiltered reads in the host system.
Data Structure：
Strong hash value of read and k-mer
SKIndex contain k-mer hash instead of k-mer
  reduce storage overhead and performance overhead of comparisions.

## Slide 14: GenStore
  GenStore-NM for Non-Matching Reads: filter most of the non-matching reads, i.e., reads that would not align to any subsequence in the reference genome. This is motivated by the fact that in read mapping, a large fraction of reads might not align to the reference genome
  Key Idea：uses chaining to build an in-storage filter.To avoid such expensive chaining, GenStore-NM selectively performs a fast version of chaining only on reads with a small number of seeds and sends other reads to the host system for full read mapping (including complete chaining).

## Slide 15: GenStore
  Overall operational flow of GenStore-NM, which consists of three steps:
  Step 1. reads the input read set from the flash chips, generates minimizer k-mers for each readand looks up each minimizer in a K-mer Index (KmerIndex) to find the potential matching locations
  Step 2. counts the number of seeds in each read to decide if the read needs to go through chaining( also filters out reads with too few seeds)
  Step 3. filters reads based on their chaining scores using a fast and efficient chaining accelerator If a read has at least one chain with a score above a specified threshold, it is sent to the CPU for mapping
Chaining score

## Slide 16: GenStore
  GenStore Flash Translation Layer (FTL)
    GenStore FTL Metadata：GenStore metadata includes the mapping information of the data structures necessary for read mapping acceleration, which enables access to the data structures without the L2P mapping table of the regular FTL.
    Data Placement：When each data structure is initially written to the SSD, GenStore sequentially and evenly distributes it across NAND flash chips.
    SSD Management Tasks：In accelerator mode, GenStore stops working as a regular SSD. It only reads data structures to perform filtering, and does not write any new data. Therefore, GenStore does not require any write-related SSD-management tasks such as garbage collection and wear-leveling.

## Slide 17: Evaluation
  Base：
    Minimap2 [Bioinformatics’18]: software mapper for short and long reads
    GenCache [MICRO’19]: hardware mapper for short reads
    Darwin [ASPLOS’18]: hardware mapper for long reads
  GS-Ext：
    Base integrated with an implementation of the GenStore filter without in-storage support.The goal of evaluating GS-Ext is to decouple the effects of GenStore’s two major benefits:
    1) alleviating I/O bottlenecks via efficient in-storage processing
    2) reducing the workload of the read mapper by filtering reads with simple operations.
    GS-Ext obtains the second benefit but not the first.
  GS：
    Base integrated with the hardware GenStore filtering accelerators, GenStore-EM and GenStore-NM

## Slide 18: Evaluation
  Area and Power (We implement GenStore’s logic components in Verilog HDL.)
    Implement GenStore’s logic components in Verilog HDL.
    Synopsys Design Compiler
    SSD power values of the Samsung 3D NAND flash-based SSD
    DRAM power values based on DDR4 model
  Performance Modeling (We evaluate hardware configurations using two simulators)
    Ramulator for DRAM timing
    MQSim for SSD timing
    Data reported in the original works for GenCache and Darwin accelerators
  Real System Results (We use real systems to evaluate all software configurations.)
    AMD EPYC 7742 CPU
    1TB DDR4 DRAM
    AMD μProf

## Slide 19: Evaluation
  SSD Configurations
    SSD-L: SATA3 interface (0.5 GB/s sequential read) (Intel SSD DC S4500 Series)
      1.2 GB/s per channel bandwidth
      8 channels
    SSD-M: PCIe Gen3 M.2 interface (3.5 GB/s sequential read)( Samsung SSD 980 PRO)
      1.2 GB/s per channel bandwidth
      16 channels
    SSD-H: PCIe Gen4 interface (7 GB/s sequential read) (Samsung SSD PM1735)
      1.2 GB/s per channel bandwidth
      16 channels
  Datasets
    SRR2052419 19.6 GB for motivation study
    Short read experiments use hg38 human reference genome
    Mason 2 genomic read simulator simulate read sets with various sizes(up to 440 GB) and different fractions of exactly-matching reads (75% and 85%)
    Use the reference genome and read set from Table 1 in Section 4.3.1

## Slide 20: Evaluation
  Area and Power Analysis
The total hardware area needed for GenStore is very small (0.20 mm2 at 65 nm and 0.02 mm2 at 14 nm, only 0.006% of a 14nm Intel Processor). The area overhead of GenStore hardware (0.06 mm2 at 32 nm) is less than 9.5% of the three 28nm ARM Cortex R4 processors in a SATA SSD controller.

## Slide 21: Evaluation
  GenStore-EM Analysis (22-GB short read and 80% of reads exactly match)
  Integration with a Software Read Mapper：1) Base (Minimap2 ), 2) SIMD, an extension of Base with a SIMD implementation of a baseline exactly-matching read filter using 128-bit SIMD instructions, 3) GS-Ext, and 4) GS.
  Integration with a Hardware Read Mapper：1) Base (GenCache), 2) GS-Ext, and 3) GS.

## Slide 22: Evaluation
  GenStore-EM Analysis
  Effect of Read Set Features on Performance：evaluate GenStore-EM while changing two key characteristics: 1) the input read set size and 2) exactly matching read rate.
  SSD-H

## Slide 23: Evaluation
  GenStore-NM Analysis：(12.4-GB read set with 99.65% of reads not aligning)
  Integration with a Software Read Mapper:1) Base (Minimap2), 2) GS
  Integration with a Hardware Read Mapper: 1) Base (Darwin), 2) GS-Ext, 3) GS.
  Effect of Read Set Features on Performance:1) input read set size, 2) alignment rates
  SSD-H

## Slide 24: Related Work
  Accelerating Read Mapping
    non-filtering approaches
      accelerate one or more non-filtering steps of read mapping (e.g., seeding and approximate string matching) using hardware accelerators. (processing-in-memory、GPUs、FPGAs、ASICs)
    filtering approaches
      accelerate the pre-alignment filtering step of read mapping. These works provide highly-parallel read filtering heuristics that quickly eliminate dissimilar sequences before invoking computationally-expensive alignment algorithms. (processing-near-memory、FPGAs、GPUs、CPUs)
  In-Storage Processing Systems
    Form：
      application-specific accelerators
      general-purpose processing inside storage devices
      SSDs closely integrated with FPGAs
      SSDs closely integrated with GPUs
      (None of these works perform in-storage filtering for read mapping to accelerate genome sequence analysis.)

## Slide 25
Thank you!

## Slide 26
collection, preparation, and sequencing of a DNA sample
basecalling
images or
electric current
reads:sequences
of nucleotides
read mapping
identifies potential matching locations of each read with respect to a known reference genome
seeding
seed filtering
chaining
sequence
alignment